USED ARTICULATED URBAN BUS

Technical Specification

This Technical Specification details the technical requirements and parameters of the used articulated urban buses to be procured. The vehicles shall operate reliably and economically within the Budapest traffic conditions. They shall have no abnormal wears nor other deficiencies nor damages hindering or excluding its intended use.

Seller shall make a statement on the technical condition of the buses and their appropriateness for operation and traffic safety. The Tenderer ensures a possibility for the detailed inspection and test drive of the vehicles in the period between submitting the bid and the announcement of the result.

- Requirements

The design and technical parameters of the vehicles shall satisfy the effective Hungarian and international requirements and rules. The vehicle shall be supplied with EC type certificate and valid technical inspection for the European Union. It shall satisfy the requirements of Decrees Nos. 5/1990 /IV.12/ KöHÉM  and 6/1990 /IV.12/ KöHÉM and 1/1990 (KHVM) and their amendments.

- Basic technical requirements

The vehicle shall be a modern, single-decker city bus of three axles, the entrance surfaces and the connecting floor surfaces shall be 100% low-floor, allowing the boarding and alighting of. wheelchair user passengers, too. All the offered vehicles shall be totally identical in finishing and equipment, thus the contingent could be considered one fleet in look and in operational aspects. An essential requirement concerning the offered vehicle type is that it shall not reduce the homogeneity of the vehicle park of the Tender Announcer, i.e. the type shall belong to one of the types already operated by BKV Zrt. or it shall be its modernized version. Moreover, the buses shall be fitted with typically heavy-duty Diesel engine, which shall meet minimum the ECE EURO 3 environmental requirements.

The driver’s cabin of the vehicle shall be fully or 50 per cent closed, comfortable – on the left hand side – and equipped with audio- and visual passenger information system. The doors shall be apt for selective opening and closing and shall be equipped with protection against seizing passengers.

| Dimensions and technical parameters, solo bus |
| --- |
| Denomination | Articulated single-decker city bus with three axles |
| Full length | Min. 17 900 mm–max. 18 400 mm |
| Full width | max. 2.550 mm |
| Full height | max. 3. 400 mm |
| Allowed total mass | 28.000 kg |
| Year of manufacturing | 2005 or later |
| Mileage performance | max. 650.000 km |
| Full capacity | min. 100+1 persons (4 persons/m2) |
| Number of passenger seats | min. 40 passenger seats (the 1,5 seats are considered as one seat) + 1 driver seat. The vehicle shall have room for a wheelchair plus a built-in ramp at one of the doors. |
| Number of passenger doors | 4 double leaf doors, originally built in by the manufacturer, out of which at least 3 doors with min. width 1200 mm |
| Step up height | max. 340 mm |
| Position angle (front, rear) | min. 7,0° |
| Engine | Heavy duty four-stroke Diesel engine, compliant with minimum ECE EURO-III. environmental requirements. |
| Gearbox | Automatic, hydraulic transmission, with minimum four forward and one reverse speeds, installed intarder (retarder) |
| Service brakes | Two-circuit brake in accordance with the provisions of UN ECE 13, equipped with ABS and a stop-brake system (which prevents starting the bus with open doors) |
| Suspension | With air springs, rigid portal axles or independent suspension, with a road saving design at the driven axle. |
| Steering system | Hydraulic power steering gear, with adjustable height and inclining design. |
| Capacity of fuel tank | It shall allow to travel 400 km per day, with single fuel fill-up, under the operating conditions of BKV Zrt. |
| Body | Chassis elements and panels shall be made of materials of increased corrosion resistance and chassis and cavity provided with anti corrosion protection |
| Equipment | Both the driver’s cab and the passenger compartment of the vehicles shall be air-conditioned. The air-conditioning shall be originally built in by the manufacturer during the manufacturing process and not subsequently fitted. |
| Passenger information system | It must be suitable for the reception and installation of the electronic passenger information system in regular service aboard the BKV Zrt. vehicles. It shall be fitted with min. 4 controlled display boards on the outside. |

## Required documents

Supplier declares that the following documents are at his disposal, which shall be handed over to the Buyer at the handover of the vehicles:

- Instruction for use and maintenance

- Instruction for repairs

- List of spare parts

- EC type certificate

- Documents (in original or copy authorized by the issuing authority) issued by the authorities of the country of origin necessary for the registration in Hungary which certify the following things:

–  	ownership of the vehicle (including the operational rights), and

- entitlement to participate in traffic (including the permits and their expiry dates required by the transport safety and environment protection authorities of the country of origin)